Intelligent Systems Club:
Rpi Workshop
Session 1:

Setup
1. Setup Windows for remote connection by going to: Control Panel → Network and Sharing Center → Change Adapter Settings → Right Click “Wifi” → Properties → “Sharing” tab → Check “Allow other network users...” → OK
2. Install WinSCP by running exe. Choose “Commander” in setup.
3. Install Netbeans from here, make sure to select under the C/C++ column.
4. Install TightVnc from here
5. Power on the RPI by plugging in the micro USB cable. Then plug in the Ethernet cable into the RPI and your laptop.
6. Login to the RPI by clicking under the “General” folder the shortcut “RPI-Login”. This will launch PuTTy.

Part 1: Learning Linux Command Line Interface (CLI)
Note: Right clicking inside the PuTTy terminal is how to Paste or the replacement for "Control + V".
This section covers some basic commands that will be very handy in using any Linux-based operating system. In general, since the Linux kernel inherits alot from the Unix kernel and many modern operating systems derive from both of these kernels, these commands are commonplace (in some form) in every operating system today, such as Windows PowerShell.
Note: These commands are being run in a terminal program, which is a running process that executes entered bash commands and also stores environmental variables, which can be used by the executing commands.

First open WinSCP → “New Site” → File protocal: SFTP → Host name “raspberrypi.mshome.net” → User name: “pi” → password “raspberrypi”.
Now copy the folder “ToRPI” from your laptop to /home/pi/Desktop by clicking and dragging the folder.

Now try some basic commands in the PuTTY terminal.
List Everything:
ls -a
Folders or files that start with "." are hidden, which is a naming convention meant to used in the background by processes without any direct user interaction.
List only some items:
ls
ls actually is the same as:
ls .
where "." refers to your 'working' or current directory.
".." refers to some directory above your working directory.
Change directory:
cd ~/Desktop
"~/Desktop" is an absolute path, where "./Desktop" is an equivalent relative path, which will resolve when your working directory is "~".
"cd .." says go up one directory level
ProTip: TAB hotkey. Hitting the tab key while typing out commands or paths will ask the OS to try to autocomplete what you are typing out. Go to the "Desktop/projects" directory and type out "cd C" then hit tab. The ongoing command should resolve to "cd Class", because there is more than one directory that begins with "Class". Hitting double tab lists the remaining possible resolutions.

Multiple commands can be run with a single paste, as with below:
cd ToRPI
cd src

There just needs to be an invisible ASCII characters "\r\n" present in the copied text, which is the same result as hitting the 'ENTER' key.
Now compile the program with:
g++ -o summon-the-devil-himself thedevil.cpp
Run the program using
./summon-the-devil-himself; echo $?
Now lets look inside the soulcontract using
nano soulcontract.txt
Exit nano (using control + X) and defy the devil himself by deleting the contract with
rm soulcontract.txt
Take a look inside the devil program with
nano thedevil.cpp
If you want to gain more knowledge about a particular command without summoning the devil, use
man ls
for the ls command, and simply replace ls with something else to learn about that.
To destroy everything you have accomplished thus far:
rm -r ../src

Part 2: Install Stuff on Linux
Method 1:
sudo apt-get update
sudo apt-get upgrade
sudo apt-get install *dependcies*
sudo apt-get install *package*
However using this method is not considered hardcore, so lets take it to the next level.
sudo apt-get install libdbus-1-dev libdbus-glib-1-dev libglib2.0-dev libical-dev libreadline-dev libudev-dev libusb-dev
cd /usr/src
sudo wget https://www.kernel.org/pub/linux/bluetooth/bluez-5.32.tar.xz
sudo tar xvf bluez-5.32.tar.xz

cd bluez-5.32
sudo ./configure --disable-systemd
sudo make
Wait 10 years, just kidding. "Control + C" will send a signal to kill the executing command.
If the make command did complete without interruption in a timely manner, run
sudo make install
To test if something is working:
sudo hcitool lescan

Part 3: Remote development using Netbeans and C/C++
Start Netbeans 8.1.

Create a sample project by going File → New Project → Samples → C/C++ → Multi Processing Application.

Now setup remote development by going to here.

Right click on the project → Properties → Run → Run command → … → Replace with
"${OUTPUT_PATH}" hello hi yes whats up no yes maybe cool wow holy how yup real fast gotta run sweet nice welp DOOM SHALL COME unlikely perhaps sortof
Then hit OK.
Now run build/run the project by clicking the Green Arrow (or hit F6).
Why is this program special? It is printing each argument using a seperate child process with the “fork()” function.